## Slide 1: Connecting Sensors to RPi
2016. 09. 22.
Jinhyuk Yim (jinhyuk@uns.ajou.ac.kr)
Eungkyu Lee (eungkyu@uns.ajou.ac.kr)

## Slide 2
Practice
  Raspberry PI GPIO tutorial
  Connects Arduino to the Raspberry Pi
Amazon Web Service (AWS)
  Introduction
  How to use AWS
  Tutorial

## Slide 3: Practice

## Slide 4: Raspberry Pi GPIO Tutorial
There are two different approaches to reading and driving the Raspberry Pi’s GPIO pins
  Python API and Examples
    RPi.GPIO API – An overview of the Python functions you can use to drive GPIO.
    RPi.GPIO Example – An example Python script that shows off both input and output functionality.
  C (and WiringPi) API and Examples
    WiringPi API – An overview of the basic functions provided by the WiringPi library.
    WiringPi Example – A simple example program that shows off WiringPi’s input and output capabilities.
  GPIO Pinout – An overview of the Pi’s GPIO header.

## Slide 5: Install WiringPi
WiringPi
  GPIO accesses library written in C language
Step 1
  Check your internet connection whether it is connected or not
    Ex) ping google.com
  Sudo apt-get update
  Sudo apt-get upgrade
  Update
    Update a “list” of available packages and versions
  Upgrade
    Upgrade “packages” to the latest version

## Slide 6: Install WiringPi
Step 2
  Sudo apt-get install git-core
Git
  Git is popular version control system designed to handle very large projects with speed and efficiency
  It is used for many open source projects.
  Ref : https://en.wikipedia.org/wiki/Git

## Slide 7: Install WiringPi
Step 3
  git clone git://git.drogon.net/wiringPi
  cd wiringPi
  ./build
Step 4
  Check your installation of wiringPI
    Type this command : “gpio –v gpio readall”

## Slide 8: Install WiringPi
Step 5
  Print GPIO map
    Type this command : “gpio readall”

## Slide 9: Ultrasonic Example
Step 1
  mkdir test
  cd test
  nano test.c
  Type the code
Step 2
  gcc –o test test.c –lwiringPi
    gcc –o <output> <sourcefile> -lwiringPi
  Execute Program
    sudo ./test

## Slide 10: UltrasonicExample
Step 3
  Connect Ultrasonic sensor to the RPi3
    VCC : 5v
    GND : Pin 06 or 09 or 25 or ...
    ECHO : GPIO23 (Pin16)
    TRIGGER : GPIO24 (Pin18)
  Execute Program
    sudo ./test

## Slide 11: Raspberry Pi Camera
Step 1
  sudo raspi-config
    Selects “Enable Camera”

## Slide 12: Raspberry Pi Camera
Step 2
  Selects “Enable” and reboot

## Slide 13: Raspberry Pi Camera
Commands
  Capture image
    raspistill –o image.jpg
  Capture video
    raspivid –o video.h264
Option
  -o <filename> : Save the file
  -t <milliseconds> : capture image after the time (Default : 5sec)
  -w,-h : set the width and the height
  -f : fullscreen preview mode

## Slide 14: Raspberry Pi camera commands

## Slide 15: Raspberry Pi Camera
Python code
  https://www.raspberrypi.org/learning/getting-started-with-picamera/worksheet/

## Slide 16: Connect Arduino to the RPi3

## Slide 17: Install Arduino IDE
Install Arduino IDE
  Sudo apt-get install Arduino
Get permission for access to the Serial port
  Sudo usermode –a –G tty pi
  Sudo usermod –a –G dialout pi
Check board and serial port (/dev/ttyACM0)

## Slide 18: Raspberry Pi code
Copy the RPI code and compile it
  Nano hello.c
    Copy and paste
  Sudo gcc –o hello hello.c –l wiringPi –DRaspberryPi
  Sudo ./hello
Check your Arduino’s port
  Dmesg | tail
#ifdef RaspberryPi
//include system librarys
#include <stdio.h> //for printf
#include <stdint.h> //uint8_t definitions
#include <stdlib.h> //for exit(int);
#include <string.h> //for errno
#include <errno.h> //error output
//wiring Pi
#include <wiringPi.h>
#include <wiringSerial.h>
// Find Serial device on Raspberry with ~ls /dev/tty*
// ARDUINO_UNO "/dev/ttyACM0"
// FTDI_PROGRAMMER "/dev/ttyUSB0"
// HARDWARE_UART "/dev/ttyAMA0"
char device[]= "/dev/ttyACM0";
// filedescriptor
int fd;
unsigned long baud = 9600;
unsigned long time=0;
//prototypes
int main(void);
void loop(void);
void setup(void);
void setup(){
printf("%s \n", "Raspberry Startup!");
fflush(stdout);
//get filedescriptor
if ((fd = serialOpen (device, baud)) < 0){
fprintf (stderr, "Unable to open serial device: %s\n", strerror (errno)) ;
exit(1); //error
}
//setup GPIO in wiringPi mode
if (wiringPiSetup () == -1){
fprintf (stdout, "Unable to start wiringPi: %s\n", strerror (errno)) ;
exit(1); //error
}
}
void loop(){
// Pong every 3 seconds
if(millis()-time>=3000){
serialPuts (fd, "Pong!\n");
// you can also write data from 0-255
// 65 is in ASCII 'A'
serialPutchar (fd, 65);
time=millis();
}
// read signal
if(serialDataAvail (fd)){
char newChar = serialGetchar (fd);
printf("%c", newChar);
fflush(stdout);
}
}
// main function for normal c++ programs on Raspberry
int main(){
setup();
while(1) loop();
return 0;
}
#endif //#ifdef RaspberryPi
Notes: #ifdef RaspberryPi
//include system librarys
#include <stdio.h> //for printf
#include <stdint.h> //uint8_t definitions
#include <stdlib.h> //for exit(int);
#include <string.h> //for errno
#include <errno.h> //error output
//wiring Pi
#include <wiringPi.h>
#include <wiringSerial.h>
// Find Serial device on Raspberry with ~ls /dev/tty*
// ARDUINO_UNO "/dev/ttyACM0"
// FTDI_PROGRAMMER "/dev/ttyUSB0"
// HARDWARE_UART "/dev/ttyAMA0"
char device[]= "/dev/ttyACM0";
// filedescriptor
int fd;
unsigned long baud = 9600;
unsigned long time=0;
//prototypes
int main(void);
void loop(void);
void setup(void);
void setup(){
printf("%s \n", "Raspberry Startup!");
fflush(stdout);
//get filedescriptor
if ((fd = serialOpen (device, baud)) < 0){
fprintf (stderr, "Unable to open serial device: %s\n", strerror (errno)) ;
exit(1); //error
}
//setup GPIO in wiringPi mode
if (wiringPiSetup () == -1){
fprintf (stdout, "Unable to start wiringPi: %s\n", strerror (errno)) ;
exit(1); //error
}
}
void loop(){
// Pong every 3 seconds
if(millis()-time>=3000){
serialPuts (fd, "Pong!\n");
// you can also write data from 0-255
// 65 is in ASCII 'A'
serialPutchar (fd, 65);
time=millis();
}
// read signal
if(serialDataAvail (fd)){
char newChar = serialGetchar (fd);
printf("%c", newChar);
fflush(stdout);
}
}
// main function for normal c++ programs on Raspberry
int main(){
setup();
while(1) loop();
return 0;
}
#endif //#ifdef RaspberryPi

## Slide 19: Arduino code
Execute Arduino IDE
  Type this code
Result

## Slide 20: Amazon Web Service (AWS)

## Slide 21: Amazon Web Service (AWS)
Amazon Web Service (AWS)
  Offers a suite of cloud-computing services that make up an on-demand computing platform
  Available from 13 regions across the world

## Slide 22: Amazon Web Service (AWS)
List of products
  Compute (Elastic Compute Cloud, EC2)
  Networking (Route53)
  Storage and content delivery (Simple Storage Service, S3)
  Database (Relational Database Service, RDS)
  Deployment (CodeDeploy)
  Management (CloudWatch)
  Application services (API Gateway)
  Analytics (Machine Learning, EMR-Hadoop, Kinesis)
  Miscellaneous (Identity and Access Management, IAM)
You can access these services using HTTP and SOAP
  HTTP: HyperText Transfer Protocol
  SOAP: Simple Object Access Protocol (using xml)

## Slide 23: How to use AWS?
http://hyeonstorage.tistory.com/145

## Slide 24: AWS IoT
http://docs.aws.amazon.com/iot/latest/developerguide/iot-device-sdk-c.html