## Slide 1: Arduino Communication
2016. 09. 06.
Jinhyuk Yim (jinhyuk@uns.ajou.ac.kr)
Eungkyu Lee (eungkyu@uns.ajou.ac.kr)

## Slide 2
Communication Interface
  Serial communication
  I2C communication
  SPI communication
  Wi-Fi communication
  Bluetooth communication
Practice

## Slide 3: Communication Interface

## Slide 4: Arduino Communications
There are lots of communication interfaces for Arduino
  I2C, Serial, Bluetooth, W-iFi …

## Slide 5: Interface types
Wired interface vs Wireless interface
  Wired interface
    Connects to the other device using cable.
      Serial communication
      Software serial communication
  Wireless interface
    Connects to the module or shield
      Wi-Fi
      Bluetooth
      Bluetooth Low Energy (BLE)

## Slide 6: Serial Communication
Serial Communication
  Also known as USB communication and UART communication
  Information passes between the computer and Arduino through the USB cable.

## Slide 7: API’s for Serial Communication
Functions for serial communication
  Serial.begin()
  Serial.end()
  Serial.available()
  Serial.read()
  Serial.peek()
  Serial.parseInt()
  Serial.write()
  Serial.flush()
If you want more information,
  https://www.arduino.cc/en/Reference/HomePage

## Slide 8: I2C Communication (1/3)
I2C (Inter-integrated circuit)
  I2C communication bus is very popular and broadly used by many electronic devices.
  it can be easily implemented in many electronic designs which require communication between a master and multiple slave devices or even multiple master devices.

## Slide 9: I2C Communication (2/3)
I2C has a master/slave protocol. The master initiates the communication.
  The sequence of events are :
  The Master device issues a start condition. This condition informs all the slave devices to listen on the serial data line for instructions.
  The Master device sends the address of the target slave device and a read/write flag.
  The Slave device with the matching address responds with an acknowledgement signal.
  Communication proceeds between the Master and the Slave on the data bus. Both the master and slave can receive or transmit data depending on whether the communication is a read or write. The transmitter sends 8-bits of data to the receiver which replies with a 1-bit acknowledgement.
  When the communication is complete, the master issues a stop condition indicating that everything is done.

## Slide 10: I2C Communication (3/3)
Connect devices using breadboard.
  SDA (Serial data)
    For data transmission
  SCL (Serial clock)
    For clock signal transmission

## Slide 11: I2C Example using two Arduino
It must share one common ground pin
  https://www.arduino.cc/en/Tutorial/MasterWriter
Master device
Slave device

## Slide 12: SPI Communication (1/2)
SPI (Serial Peripheral Interface)
  A synchronous serial communication interface used for short distance communication
  Communicate in Full-Duplex mode using master-slave architecture with single master
  Commonly used to send data between microcontrollers and small peripherals such as shift registers, sensors, and SD cards
    SCLK: Serial Clock (output from master)
    MOSI: Master Output, Slave Input (output from master)
    MISO: Master Input, Slave Output (output from slave)
    SS: Slave Select (output from master)

## Slide 13: SPI Communication (2/2)
Two types of slave
  Independent
    Independent slave select line exists
  Daisy-chain
    1st slave’s output becomes 2nd slave’s input
    Act like shift register
Typical SPI bus
3 independent slaves
Daisy-chained SPI bus
3 cooperative slaves

## Slide 14: Wi-Fi Communication
Wi-Fi
  Technology that allows electronic devices to connect to a wireless LAN (WLAN) network
Wi-Fi devices for Arduino
  The Arduino Wi-Fi Shield / Module allows an Arduino board to connect to the internet using the 802.11 wireless specification
  Wi-Fi shield
    Mount the Wi-Fi Shield on the headers of Arduino.
  Wi-Fi module
    Connects the Arduino using cable.
Arduino Wi-Fi Module
Arduino UNO
Arduino Wi-Fi Shield

## Slide 15: API’s for Wi-Fi Communication
WiFi class
  The WiFi class initializes the Ethernet library and network settings
    Wifi.begin()
    Wifi.disconnect()
    Wifi.config()
    Wifi.setDNS()
    Wifi.SSID()
    Wifi.BSSID()
    Wifi.RSSI()
    Wifi.encryptionType()
    Wifi.scanNetworks()
    Wifi.status()
    Wifi.getSocket()
    Wifi.macAddress()
If you want more information,
    https://www.arduino.cc/en/Reference/WiFi

## Slide 16: Bluetooth Communication (1/2)
Bluetooth
  Bluetooth is a wireless technology standard for exchanging data over short distances from fixed and mobile devices. And one of the popular wireless communication technologies because of its low power consumption, low cost.
Master and Slaves
  Bluetooth networks use a master/slave model to control when and where devices can send data.
  The master can send data to any of its slaves and request data from them as well.
  Slaves are only allowed to transmit to and receive from their master.

## Slide 17: Bluetooth Communication (2/2)
Bluetooth devices for Arduino
  Bluetooth module
    Connects the Arduino using cable.
  Bluetooth shield
    Mount the Bluetooth Shield on the headers of Arduino.

## Slide 18: API’s for Bluetooth Communication
Using Software serial communication

## Slide 19: Practice

## Slide 20: Practice #1 – Serial communication
Control the LED through serial communication
  Enter the number that how long the LED will blink.
  Function for serial communication (PC to Arduino)
    Serial.available()
      Get the number of bytes (characters) available for reading from the serial port.
    Serial.read()
      Reads incoming serial data.
    Serial.peek()
      Returns the next byte (character) of incoming serial data without removing it from the internal serial buffer.
    Serial.parseInt()
      Returns the first valid (long) integer number from the serial buffer.