## Slide 1: Raspberry Pi Basic
2016. 09. 20.
Jinhyuk Yim (jinhyuk@uns.ajou.ac.kr)
Eungkyu Lee (eungkyu@uns.ajou.ac.kr)

## Slide 2
Introduction to Raspberry Pi
  Raspberry Pi
  Arduino & Raspberry Pi
  Raspberry Pi’s OS & model
  Raspberry Pi Specification
  Raspberry Pi GPIO
Practice

## Slide 3: Introduction

## Slide 4: Raspberry Pi
The Raspberry Pi is a single-board computers developed in the United Kingdom by the Raspberry Pi Foundation to promote the teaching of basic computer science in schools and developing countries.

## Slide 5: Arduino & Raspberry Pi
 | Arduino Uno | Raspberry Pi
CPU type | Micro controller | Micro processor
Operating System | None | Linux (usually Raspbian)
Disk | 32kbyte | Depends on SD card
Other connectivity | None | USB, Ethernet, HDMI, Audio

## Slide 6: Introduction to Raspberry Pi
Operating System
  NOOBS
  RASPBIAN
  UBUNTU MATE
  WINDOWS 10 IOT CORE
Hardware Model & Version
  Model A (1, 1+)
  Model B (1, 1+, 2, 3)
  Model Zero (N/A)
Ref : https://www.raspberrypi.org

## Slide 7: Raspberry Pi Specification

## Slide 8: Raspberry Pi GPIO

## Slide 9: Practice

## Slide 10: Install Raspbian
Download Raspbian image
  https://www.raspberrypi.org/downloads/raspbian/

## Slide 11: Install Raspbian
Download Win32 Disk Imager
  https://sourceforge.net/projects/win32diskimager/

## Slide 12: Install Raspbian
Write image on SD card
  Execute Disk imager and set the location of image

## Slide 13: Install Raspbian
Configure Raspberry Pi
  Connect your SD card to the PC and modify “cmdline.txt” file
  Append your IP address behind “rootwait” (ip=192.168.2.2)
    This is IP address for your Raspberry Pi

## Slide 14: Install Raspbian
Configure your laptop
  Open Network connections – Ethernet adapter – [Properties]
  Click Internet Protocol Version 4(TCP/IPv4)’s Properties
  Selects “Use the following IP address” and then change your IP address as below.

## Slide 15: Install Raspbian
Download Putty
  http://www.chiark.greenend.org.uk/~sgtatham/putty/download.html
  Install putty.exe

## Slide 16: Install Raspbian
Connect Raspberry Pi and your laptop using Ethernet cable
  Insert your SD card to your Raspberry Pi
  Connect Raspberry Pi and your laptop using Ethernet cable
  Power the Raspberry Pi on
Execute Putty
  Type your IP address on the Host Name field
Save the session information
  For your convenience...

## Slide 17: Install Raspbian
Access to the Raspberry Pi
  ID : pi / PW : raspberry

## Slide 18: Install Raspbian
Configure wireless LAN
  Check wireless LAN interfaces and Add wlan0 interface
    sudo vi /etc/network/interfaces
    Add below information
    (if you already have this information skip)
  Scan Network
    sudo iwlist wlan0 scan
allow-hotplug wlan0
iface wlan0 inet dhcp
wpa-conf /etc/wpa_supplicant/wpa_supplicant.conf
iface default inet dhcp

## Slide 19: Install Raspbian
Configure Wireless LAN
  Add wireless network information
    sudo vi /etc/wpa_supplicant/wpa_supplicant.conf
    If there are no password then type “key_mgmt=NONE”
  Save the file and reboot
    sudo reboot

## Slide 20: Configuring development environment
Configuring remote Desktop connection
  xrdp
    Open source remote access protocol based on RDP (Remote Desktop Protocol) which developed by Microsoft.
    It provides remote access for the Raspberry Pi’s GUI environment
Install xrdp
  Sudo apt-get install xrdp
Access the Raspberry Pi at the Window
  Start menu-Search-Remote Desktop Connection and type ip/password

## Slide 21: Configuring development environment
Now we can access the Raspberry Pi’s GUI environment remotely